Addendum

Installation Guide

Here are some changes made to the install guide to help make the installation easier-

Step #7-b.  Do not completely tighten factory 10mm Nut- you will need a little play in the bracket’s angle later when the enclosure is mounted.   This factory 10mm nut will be tightened later.

Step #11-c.  Do not completely tighten both nuts- just slightly tighten, only finger tight.

Step #12-b.  Before tightening the double bolt assembly ensure your UD Sub Enclosure is fitted into the proper mounting location- here are the three factors to help you determine if you have correct placement.

1). The Clutch must clear! – There should not be any interaction between the UD Sub Enclosure and the clutch.

2). The top of the enclosure will touch the round metal framing- the same metal bar the Flex bracket mounts to. See step 7.  There are 3 pictures here that portray the bar in reference.

3). The Flex Bracket will actually determine how much too left side the enclosure will be.  You want your UD Sub Enclosure, as far to the left as the Flex bracket will permit.

Tighten all four UD Sub Enclosures mounting points when you are certain the UD Sub Box is fitted properly (from above notes). Tighten the four points in the same order as the install guide.

Now Tighten 10mm factory nut from step 7.

# Special instructions for the 2001 MR2 Spyder

There is a black keyless entry module bolted next to your BCM module. – This is in the way and needs to be moved.  The keyless module will fit above your coin holder.  Take these steps to install the UD Sub in the 2001 MR2 Spyder.

- Remove the keyless entry module.

- Remove the factory mounting brackets from the keyless module.

*** Test fit your module next to the coin holder before applying double sided tape.

- Apply double sided tape to module.

- Mount the keyless module to the right  of the change holder where it is flat.

The double sided tape is inside your parts envolope.